## Slide 1
CS44 Data Communications

## Slide 2
PROTOCOL LAYERING
  Scenarios
  Principles of Protocol Layering
  Logical Connections
TCP/IP PROTOCOL SUITE
  Layered Architecture
  Layers in the TCP/IP Protocol Suite
  Description of Each Layer
  Encapsulation and Decapsulation
  Addressing
  Multiplexing and Demultiplexing
THE OSI MODEL
  OSI versus TCP/IP
  Lack of OSI Model’s Success

## Slide 3
Direct communication
  Most basic form of communication
Serial Port
TX
RX
TX RX
GND GND
Internet communication
  Communication is performed over the Internet
Internet

## Slide 4
But what's going on underneath?
  What is inside the "cloud"?
    Computer Network in broad sense
Internet
A
B
Two network applications should interact as if they were directly connected
write read
App App

## Slide 5
Two models have been devised to define computer network
operations:
  TCP/IP protocol suite
  OSI model
Protocol layering is used in both models
  protocol defines the rules that both the sender and receiver and all
intermediate devices need to follow to be able to communicate effectively
  Simple communication - may need only one simple protocol
  Complex communication - may need to divide the task between different layers
    a protocol at each layer - protocol layering
      Protocol layering enables us to divide a complex task into several smaller and simpler tasks
Let us develop two simple scenarios to better understand the need
for protocol layering
  Simple communication: in Daily Life
  Complex communication: in Daily Life

## Slide 6
Assume Maria and Ann are neighbors with a lot of common ideas
Communication between Maria and Ann takes place in one layer, face to face, in the same language
  A single-layer protocol - set of rules needs to be followed
    greet each other when they meet.
    confine their vocabulary to the level of their friendship
    refrain from speaking when the other party is speaking
    conversation should be a dialog, not a monolog: both should have the opportunity to talk about the issue
    exchange some nice words when they leave.

## Slide 7
two friends who communicate through postal mail
  The process of sending a letter to a friend would be complex if there were no services available from the post office.
Tasks involved in sending a letter

## Slide 9
Computer networks are complex systems
  Tasks involve varieties of hardware and software components, and protocols
Networking task is divided into several subtasks
  I.e., several layers

## Slide 10
Allows to separate the services from the implementation
  A layer needs to be able to receive a set of services from the lower layer and to give the services to the upper layer; don’t care about how the layer is implemented.
  Layer N uses services provided by Layer N-1
Layer N
Layer N
Using services
Providing services
Layer N-2
Layer N-2
Layer N-1
Layer N-1
Communication System
Logical communication path
Layer N protocol

## Slide 11
Transmission Control Protocol/Internet Protocol
a set of protocols organized in different layers
used in the Internet today
a hierarchical protocol: means that each upper level protocol is supported by the services provided by one or more lower level protocols
A protocol defines the rules that both the sender and receiver and all intermediate devices need to follow to be able to communicate effectively.

## Slide 12: Layers in TCP/IP Protocol Suite
The original TCP/IP protocol suite was defined as four software layers built upon the hardware.
Today, TCP/IP is thought of as a five- layer model.

## Slide 13
To show how the layers in the TCP/IP protocol works, we assume that we have following internet
  use the suite in a small internet made up of three LANs (links) - each with a link-layer switch.
  links are connected by one router
router -> 3-layers
link-layer switch ->2-layers

## Slide 14
To understand the duty of each layer, we need to think about the logical connections between layers.
The duty of the application, transport, and network layers is end-to-end.
Their domain of duty is the internet.
The duty of the data-link and physical layers
is hop-to-hop, hop is a host or router.
Their domain of duty is the link.

## Slide 15
the second principle: identical objects below each layer related to each device.

## Slide 16
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
The Internet Protocol Stack
User
Transmission
Medium
Hardware
Software

## Slide 17
The only layer to interact with user
SMTP
HTTP
FTP
SMTP
HTTP
FTP
Data
Data H5
Application
Layer
to Transport
from Transport
Data H5
Data
Communication System
Logical communication

## Slide 18
Duties/services
  Port addressing
  Segmentation and reassembly
  Connection control
  Flow control (end-to-end)
  Error control (end-to-end)

## Slide 19
Transport Layer
Data
Data1
Data3 H4
H4 Data2 H4
(segments)
to Network
Data
Data1
H4 Data2
H4 Data3 H4
from Network
Process
Process
…
Process
Process
…
PORT #
PORT #

## Slide 20
Duties/services
  Logical addressing
  Routing

## Slide 21
Network Layer
Data
from Transport
to Data Link
Data
to Transport
from Data Link
Data
H3
Data
H3
(packet)

## Slide 22
Network A
Network B
B.6
B.1
B.3
Network C
C.7
C.2
Network D
D.8
D.3
A.1, A.2, B.1, B.3, ... are logical addresses
R3
R2
A.5
R1
B.7
B.2
D.1 Router
B.9
C.3
Data | A1 | C7
Data | A1 | C7
Data | A1 | C7
To transport layer
From transport layer
Data A1 C7
A.1 A.2

## Slide 23
Duties/services
  Framing
  Physical addressing
  Flow control (hop-to-hop)
  Error control (hop-to-hop)
  Access control

## Slide 24
Data Link
Layer
Data
from Network
to Physical
Data
to Network
from Physical
Data
H2
Data
H2
(frame)
T2
T2

## Slide 25
3B
9F, 3B, 82, 6D, ... are physical addresses
9F
82
6D
T2 | Data | 9F 6D
Data
H2

## Slide 26
Network B
Network C
B.6
B.3
C.7
C.2
Network D
D.8
D.3
79
62
54
74
Data | A.1 | C.7 | 97 | 25
Data | A.1 | C.7 | 79 | 62
Data A.1 C.7 54 74
R3
R2
Data A.1 C.7 54 74
To network layer
Data A.1 C.7
A.1 A.2
97 32 Network A
25 A.5
R1
B.7 B.1
12 B.2
88 D.1
B.9
C.3

## Slide 27
Duties/services
  Physical characteristics of interfaces and media
  Representation of bits
  Data rate (transmission rate)
  Synchronization of bits

## Slide 28
 | Data | 
 | 01001011 | 
(bits) |  | 
Physical
Layer
from Data Link
 | Data | 
 | 01001011 | 
to Data Link
Transmission medium

## Slide 30
L5 data
H5
L4 data
H4
L3 data
H3
L2 data
T2
H2
0111011010101001010101001
L5 data
H5
L4 data
H4
L3 data
H3
L2 data
T2
H2
0111010101010010101010101
5
4
3
2
1
5
4
3
2
1
Transmission medium

## Slide 31
Any communication that involves two parties needs two addresses: source address and destination address.
Although it looks as if we need five pairs of addresses, one pair per layer, we normally have only four because the physical layer does not need addresses; the unit of data exchange at the physical layer is a bit, which definitely cannot have an address.

## Slide 33
Since the TCP/IP protocol suite uses several protocols at some layers, we can say that we have multiplexing at the source and demultiplexing at the destination.
Multiplexing in this case means that a protocol at a layer can encapsulate a packet from several next-higher layer protocols (one at a time).
Demultiplexing means that a protocol can decapsulate and deliver a packet to several next-higher layer protocols (one at a time

## Slide 34
To be able to multiplex and demultiplex, a protocol needs to have a field in its header to identify to which protocol the encapsulated packets belong.
Ex: At the transport layer, either UDP or TCP can accept a message from several application-layer protocols.

## Slide 35
Layer | Protocols
Application | HTTP, FTP, Telnet, SMTP, ...
Transport | TCP, UDP, SCTP, ...
Network | IP (IPv4), IPv6, ICMP, IGMP, ...
Data Link | Ethernet, Wi-Fi, PPP, ...
Physical | RS-232, DSL, 10Base-T, ...

## Slide 36
OSI – Open Systems Interconnection
Developed by the International Standards Organizations (ISO)
7.Application Layer
6.Presentation Layer
5.Session Layer
4.Transport Layer
3.Network Layer
2.Data Link Layer
1.Physical Layer
User
Two additional layers
  Presentation layer
  Session layer
Transmission Medium

## Slide 37
Duties/services
  Interaction management
    Simplex, half-duplex, full-duplex
  Session recovery

## Slide 39
When we compare the two models, we find that two layers, session and presentation, are missing from the TCP/IP protocol suite. These two layers were not added to the TCP/IP protocol suite after the publication of the OSI model. The application layer in the suite is usually considered to be the combination of three layers in the OSI model

## Slide 40
The OSI model appeared after the TCP/IP protocol suite. Most
experts were at first excited and thought that the TCP/IP protocol
would be fully replaced by the OSI model. This did not happen for
several reasons, but we describe only three, which are agreed upon by all experts in the field:
1. OSI was completed when TCP/IP was fully in place. changing it would cost a lot.
2. some layers in the OSI model were never fully defined. For example, although the services provided by the presentation and the session layers were listed in the document, actual protocols for these two layers were not fully defined, nor were they fully described, and the corresponding software was not fully developed.
3. when OSI was implemented by an organization in a different application, it did not show a high enough level of performance to entice the Internet authority to switch from the TCP/IP protocol suite to the OSI model.

## Slide 41
Layered tasks are used for complex communication details
Layer models were created for reference
  Internet model
  ISO's OSI model
Protocol suite is a collection of protocols operating at various layers