## Slide 1: Unit I Chapter 3 Physical Layer
Reference: Data Communication and Networking, Behrouz A Forouzan, McGraw Hill, 5th Edition,
2008.

## Slide 2: 3.5 DATA RATE LIMITS
A very important consideration in data communications is how fast we can send data, in bits per second, over a channel.
Data rate depends on three factors:
  1. The bandwidth available
  2. The level of the signals we use
  3. The quality of the channel (the level of noise)
Two theoretical formulas were developed to calculate the data rate: one by Nyquist for a noiseless channel, another by Shannon for a noisy channel.

## Slide 3: 3.5.1 Noiseless Channel: Nyquist Bit Rate
For a noiseless channel, the Nyquist bit rate formula defines the theoretical maximum bit rate
In this formula, bandwidth is the bandwidth of the channel, L is the number of signal levels used to represent data, and BitRate is the bit rate in bits per second.
According to the formula, we might think that, given a specific bandwidth, we can have any bit rate we want by increasing the number of signal levels. Although the idea is theoretically correct, practically there is a limit.
When we increase the number of signal levels, we impose a burden on the receiver. If the number of levels in a signal is just 2, the receiver can easily distinguish between a 0 and a 1. If the level of a signal is 64, the receiver must be very sophisticated to distinguish between 64 different levels.
In other words, increasing the levels of a signal reduces the reliability of the system.

## Slide 4: 3.5.1 Noiseless Channel: Nyquist Bit Rate Contd.
Example 3.34
Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels. The maximum bit rate can be calculated as

## Slide 5: 3.5.1 Noiseless Channel: Nyquist Bit Rate Contd.
Example 3.34
Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels. The maximum bit rate can be calculated as

## Slide 6: 3.5.1 Noiseless Channel: Nyquist Bit Rate Contd.
Example 3.35
Consider the same noiseless channel transmitting a signal with four signal levels (for each level, we send 2 bits). The maximum bit rate can be calculated as

## Slide 7: 3.5.1 Noiseless Channel: Nyquist Bit Rate Contd.
Example 3.35
Consider the same noiseless channel transmitting a signal with four signal levels (for each level, we send 2 bits). The maximum bit rate can be calculated as

## Slide 8: 3.5.1 Noiseless Channel: Nyquist Bit Rate Contd.
Example 3.36
We need to send 265 kbps over a noiseless channel with a bandwidth of 20 kHz. How many signal levels do we need?

## Slide 9: 3.5.1 Noiseless Channel: Nyquist Bit Rate Contd.
Example 3.36
We need to send 265 kbps over a noiseless channel with a bandwidth of 20 kHz. How many signal levels do we need?
Solution
We can use the Nyquist formula as shown:
Since this result is not a power of 2, we need to either increase the number of levels or reduce the bit rate. If we have 128 levels, the bit rate is 280 kbps. If we have 64 levels, the bit rate is 240 kbps.

## Slide 10: 3.5.2 Noisy Channel: Shannon Capacity
In reality, we cannot have a noiseless channel; the channel is always noisy.
In 1944, Claude Shannon introduced a formula, called the Shannon capacity, to determine the theoretical highest data rate for a noisy channel:
In this formula, bandwidth is the bandwidth of the channel, SNR is the signal-to-noise ratio, and capacity is the capacity of the channel in bits per second.
Note that in the Shannon formula there is no indication of the signal level, which means that no matter how many levels we have, we cannot achieve a data rate higher than the capacity of the channel.

## Slide 11: 3.5.2 Noisy Channel: Shannon Capacity Contd.
Example 3.37
Consider an extremely noisy channel in which the value of the signal-to-noise ratio is almost zero. In other words, the noise is so strong that the signal is faint. For this channel the capacity C is calculated as
This means that the capacity of this channel is zero regardless of the bandwidth.
In other words, we cannot receive any data through this channel.

## Slide 12: 3.5.2 Noisy Channel: Shannon Capacity Contd.
Example 3.38
We can calculate the theoretical highest bit rate of a regular telephone line. A telephone line normally has a bandwidth of 3000 Hz (300 to 3300 Hz) assigned for data communications.
The signal-to-noise ratio is usually 3162. For this channel the capacity is calculated as
This means that the highest bit rate for a telephone line is 34.860 kbps.
If we want to send data faster than this, we can either increase the bandwidth of the line or improve the signal-to-noise ratio.

## Slide 13
A line has a signal-to-noise ratio of 1000 and a bandwidth of 4000 KHz. What is the maximum data rate supported by this line?

## Slide 14
A line has a signal-to-noise ratio of 1000 and a bandwidth of 4000 KHz. What is the maximum data rate supported by this line?

## Slide 15
We measure the performance of a telephone line (4 KHz of bandwidth). When the signal is 10 V, the noise is 5 mV. What is the maximum data rate supported by this telephone line?

## Slide 16
We measure the performance of a telephone line (4 KHz of bandwidth). When the signal is 10 V, the noise is 5 mV. What is the maximum data rate supported by this telephone line?
SNR = (10)^2 / (5x10^-3) ^2 =4 x 10^6
C = 4 x 10^3 x log2 (1+4 x 10^6)
= 87.72 kbps

## Slide 17: 3.5.2 Noisy Channel: Shannon Capacity Contd.
Example 3.39
The signal-to-noise ratio is often given in decibels. Assume that SNRdB = 36 and the channel bandwidth is 2 MHz.
The theoretical channel capacity can be calculated as

## Slide 18: 3.5.2 Noisy Channel: Shannon Capacity Contd.
Example 3.40
When the SNR is very high, we can assume that SNR + 1 is almost the same as SNR. In these cases, the theoretical channel capacity can be simplified to
For example, we can calculate the theoretical capacity of the previous example as

## Slide 19
What is the theoretical capacity of a channel in each of the following cases?
  a. Bandwidth: 20 KHz SNRdB = 40
  b. Bandwidth: 200 KHz SNRdB = 4
  c. Bandwidth: 1 MHz SNRdB = 20

## Slide 20
What is the theoretical capacity of a channel in each of the following cases?
  a. Bandwidth: 20 KHz SNRdB = 40
  b. Bandwidth: 200 KHz SNRdB = 4
  c. Bandwidth: 1 MHz SNRdB = 20

## Slide 21
We have a channel with 4 KHz bandwidth. If we want to send data at 100Kbps, what is the minimum SNRdB? What is the SNR?

## Slide 22
We have a channel with 4 KHz bandwidth. If we want to send data at 100Kbps, what is the minimum SNRdB? What is the SNR?

## Slide 23: 3.5.3 Using Both Limits
We have a channel with a 1-MHz bandwidth. The SNR for this channel is 63. What are the appropriate bit rate and signal level?
First, we use the Shannon formula to find the upper limit.
The Shannon formula gives us 6 Mbps, the upper limit. For better performance we choose something lower, 4 Mbps, for example.
Then we use the Nyquist formula to find the number of signal levels.
The Shannon capacity gives us the upper limit; the Nyquist formula tells us how many signal levels we need.

## Slide 24: 3.6 PERFORMANCE
One important issue in networking is the performance of the network—how good is it?
  Bandwidth
  Throughput
  Latency (Delay)
  Bandwidth-Delay Product
  Jitter

## Slide 25: 3.6.1 Bandwidth
One characteristic that measures network performance is bandwidth.
However, the term can be used in two different contexts with two different measuring values: bandwidth in hertz and bandwidth in bits per second.
Bandwidth in Hertz
Bandwidth in hertz is the range of frequencies contained in a composite signal or the range of frequencies a channel can pass.
For example, we can say the bandwidth of a subscriber telephone line is 4 kHz.

## Slide 26: 3.6.1 Bandwidth Contd.
Bandwidth in Bits per Seconds
The term bandwidth can also refer to the number of bits per second that a channel, a link, or even a network can transmit.
For example, one can say the bandwidth of a Fast Ethernet network (or the links in this network) is a maximum of 100 Mbps.
This means that this network can send 100 Mbps.
Relationship
There is an explicit relationship between the bandwidth in hertz and bandwidth in bits per second.
Basically, an increase in bandwidth in hertz means an increase in bandwidth in bits per second.

## Slide 27: 3.6.1 Bandwidth Contd.
Example 3.42
The bandwidth of a subscriber line is 4 kHz for voice or data. The bandwidth of this line for data transmission can be up to 56,000 bps using a sophisticated modem to change the digital signal to analog.
Example 3.43
If the telephone company improves the quality of the line and increases the bandwidth to 8 kHz, we can send 112,000 bps by using the same technology as mentioned in Example 3.42.

## Slide 28: 3.6.2 Throughput
The throughput is a measure of how fast we can actually send data through a network.
A link may have a bandwidth of B bps, but we can only send T bps through this link with T always less than B.
In other words, the bandwidth is a potential measurement of a link; the throughput is an actual measurement of how fast we can send data.
For example, we may have a link with a bandwidth of 1 Mbps, but the devices connected to the end of the link may handle only 200 kbps.
This means that we cannot send more than 200 kbps through this link.

## Slide 29: 3.6.2 Throughput Contd.
Example 3.44
A network with bandwidth of 10 Mbps can pass only an average of 12,000 frames per minute with each frame carrying an average of 10,000 bits. What is the throughput of this network?
Solution
We can calculate the throughput as
The throughput is almost one-fifth of the bandwidth in this case.

## Slide 30: 3.6.3 Latency (Delay)
The latency or delay defines how long it takes for an entire message to completely arrive at the destination from the time the first bit is sent out from the source.
We can say that latency is made of four components: propagation time, transmission time, queuing time and processing delay.

## Slide 31: 3.6.3 Latency (Delay) Contd.
Propagation Time
Propagation time measures the time required for a bit to travel from the source to the destination.
The propagation time is calculated by dividing the distance by the propagation speed.
The propagation speed of electromagnetic signals depends on the medium and on the frequency of the signal. For example, in a vacuum, light is propagated with a speed of 3 × 10^8 m/s. It is lower in air; it is much lower in cable

## Slide 32: 3.6.3 Latency (Delay) Contd.
Example 3.45
What is the propagation time if the distance between the two points is 12,000 km? Assume the propagation speed to be 2.4 × 10^8 m/s in cable.
Solution
We can calculate the propagation time as
The example shows that a bit can go over the Atlantic Ocean in only 50 ms if there is a direct cable between the source and the destination.

## Slide 33: 3.6.3 Latency (Delay) Contd.
Transmission Time
In data communications we don’t send just 1 bit, we send a message.
The first bit may take a time equal to the propagation time to reach its destination; the last bit also may take the same amount of time.
However, there is a time between the first bit leaving the sender and the last bit arriving at the receiver. The first bit leaves earlier and arrives earlier; the last bit leaves later and arrives later.
The transmission time of a message depends on the size of the message and the bandwidth of the channel.

## Slide 34
If the bandwidth of the channel is 5 Kbps, how long does it take to send a frame of 100,000 bits out of this device?

## Slide 35
If the bandwidth of the channel is 5 Kbps, how long does it take to send a frame of 100,000 bits out of this device?

## Slide 36
What is the transmission time of a packet sent by a station if the length of the packet is 1 million bytes and the bandwidth of the channel is 200 Kbps?

## Slide 37
What is the transmission time of a packet sent by a station if the length of the packet is 1 million bytes and the bandwidth of the channel is 200 Kbps?

## Slide 38
Example 3.46
What are the propagation time and the transmission time for a 2.5-KB (kilobyte) message (an email) if the bandwidth of the network is 1 Gbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 10^8 m/s.

## Slide 39
Example 3.46
What are the propagation time and the transmission time for a 2.5-KB (kilobyte) message (an email) if the bandwidth of the network is 1 Gbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 10^8 m/s.

## Slide 40
What are the propagation time and the transmission time for a 5-MB (megabyte) message (an image) if the bandwidth of the network is 1 Mbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 10^8 m/s.

## Slide 41
What are the propagation time and the transmission time for a 5-MB (megabyte) message (an image) if the bandwidth of the network is 1 Mbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 10^8 m/s.

## Slide 42: 3.6.3 Latency (Delay) Contd.
Queuing Time
The third component in latency is the queuing time, the time needed for each intermediate or end device to hold the message before it can be processed.
The queuing time is not a fixed factor; it changes with the load imposed on the network.
When there is heavy traffic on the network, the queuing time increases.
An intermediate device, such as a router, queues the arrived messages and processes them one by one. If there are many messages, each message will have to wait.

## Slide 43
What is the total delay (latency) for a frame of size 5 million bits that is being sent on a link with 10 routers each having a queuing time of 2 μs and a processing time of 1 μs. The length of the link is 2000 Km. The speed of light inside the link is 2 × 108 m/s. The link has a bandwidth of 5 Mbps. Which component of the total delay is dominant? Which one is negligible?

## Slide 44
What is the total delay (latency) for a frame of size 5 million bits that is being sent on a link with 10 routers each having a queuing time of 2 μs and a processing time of 1 μs. The length of the link is 2000 Km. The speed of light inside the link is 2 × 108 m/s. The link has a bandwidth of 5 Mbps. Which component of the total delay is dominant? Which one is negligible?

## Slide 45: 3.6.4 Bandwidth-Delay Product
Bandwidth and delay are two performance metrics of a link.
In data communications the product of the two, the bandwidth-delay product is important.
Let us elaborate on this issue, using two hypothetical cases as examples.
❑ Case 1. Figure 3.32 shows case 1.
  Let us assume that we have a link with a bandwidth of 1 bps.
  We also assume that the delay of the link is 5
  We want to see what the bandwidth-delay product means in this case.
  Looking at the figure, we can say that this product 1 × 5 is the maximum number of bits that can fill the link. There can be no more than 5 bits at any time on the link.

## Slide 46: 3.6.4 Bandwidth-Delay Product Contd.

## Slide 47: 3.6.4 Bandwidth-Delay Product Contd.
Case 2.
Now assume we have a bandwidth of 5 bps.
Figure 3.33 shows that there can be maximum 5 × 5 = 25 bits on the line.
The reason is that, at each second, there are 5 bits on the line; the duration of each bit is 0.20 s.

## Slide 48: 3.6.4 Bandwidth-Delay Product Contd.
The above two cases show that the product of bandwidth and delay is the number of bits that can fill the link.
This measurement is important if we need to send data in bursts and wait for the acknowledgment of each burst before sending the next one.
To use the maximum capability of the link, we need to make the size of our burst 2 times the product of bandwidth and delay; we need to fill up the full-duplex channel (two directions).
The sender should send a burst of data of (2 × bandwidth × delay) bits.
The sender then waits for receiver acknowledgment for part of the burst before sending another burst.
The amount 2 × bandwidth × delay is the number of bits that can be in transition at any time.

## Slide 49: 3.6.4 Bandwidth-Delay Product Contd.
Example 3.48
We can think about the link between two points as a pipe. The cross section of the pipe represents the bandwidth, and the length of the pipe represents the delay.
We can say the volume of the pipe defines the bandwidth-delay product, as shown in Figure 3.34.

## Slide 50: 3.6.5 Jitter
Another performance issue that is related to delay is jitter.
We can roughly say that jitter is a problem if different packets of data encounter different delays and the application using the data at the receiver site is time-sensitive (audio and video data, for example).
If the delay for the first packet is 20 ms, for the second is 45 ms, and for the third is 40 ms, then the real-time application that uses the packets endures jitter.

## Slide 51: END of Chapter 3