## Slide 1: Analog Transmission
CS44 Data Communications

## Slide 2: Outline
2
Digital-to-analog Conversion
  Aspects of Digital-to-Analog Conversion
  Amplitude Shift Keying
  Frequency Shift Keying
Analog-to-analog Conversion
  Amplitude Modulation (AM)
  Frequency Modulation (FM)
  Phase Modulation (PM)

## Slide 3: Analog Vs Digital
 | Analog Signal | Digital Signal | 
 | a continuous wave that changes over a time period. | a discrete wave that carries information in binary form. | 
 | represented by a sine wave. | represented by square waves. | 
 | described by the amplitude, period or frequency, and phase. | described by bit rate and bit intervals. | 
 | has no fixed range. | has a finite range i.e. between 0 and 1. | 
 | more prone to distortion. | less prone to distortion. | 
 | transmit data in the form of a wave. | carries data in the binary form i.e. 0 and 1. | 
 | The human voice is the best example of an analog signal. | Signals used for transmission in a computer are the digital signal. | 
 | analog transmission is the only choice if we have a bandpass channel. | while digital transmission is very desirable, a low- pass channel is needed. | 
 | Converting a low-pass analog signal to a bandpass analog signal is traditionally called analog-to-analog conversion. | Converting digital data to a bandpass analog signal is traditionally called digital-to-analog conversion. | 
 |  | 5 | 

## Slide 4: Analog-to-analog conversion
6
Change an analog signal to a new analog signal with a smaller bandwidth
  used when only a band-pass channel is available
Three methods:
  Amplitude modulation (AM) : amplitude of a carrier is changed
based on the changes in the original analog signal
  Frequency modulation (FM): the phase of a carrier is changed
based on the changes in the original analog signal
  Phase modulation (PM): the phase of a carrier signal is changed to show the changes in the original signal

## Slide 5: Digital-to-Analog Conversion
Digital-to-analog conversion is the process of changing one of the characteristics of an analog signal based on the information in digital data when a band-pass channel is available
Required to send digital data over a band-pass channel
  Also known as modulation
(band-pass channel)

## Slide 6: Digital-to-analog conversion
Four methods:
  Amplitude shift keying (ASK): amplitude of a carrier is changed using the
digital data
  Frequency shift keying (FSK): frequency of a carrier is changed using the
digital data.
  Phase shift keying (PSK): phase of a carrier signal is changed to represent
digital data.
  Quadrature amplitude modulation (QAM): both amplitude and phase
of a carrier signal are changed to represent digital data.

## Slide 7: Amplitude shift keying
Amplitude of the carrier signal is varied to create signal elements
Both frequency and phase remain constant while the amplitude changes
Binary ASK (BASK)
  uses only two amplitude levels
Multilevel ASK (implemented with QAM)
  more than two levels

## Slide 8: Binary Amplitude Shift Keying
Several levels (kinds) of signal elements with a different amplitude can exists
ASK  normally implemented using only two levels
  Binary amplitude shift keying or on-off keying (OOK)
  Peak amplitude of
    One signal level is 0
    Other signal level is the same as the amplitude of the carrier frequency
middle of the bandwidth - fc : Carrier frequency
0 < d < 1

## Slide 9: Bandwidth for ASK
carrier signal is only one simple sine wave -> has a continuous set of frequencies
modulation produces a nonperiodic composite signal
bandwidth is proportional to the signal rate (baud rate)
B = (1 + d) x S
  S is the signal rate
  B is the bandwidth
  d depends on the modulation and filtering process
  The value of d is between 0 and 1
min
B =S
Bmax=2S
Minimum Bandwidth = S
fc
fc-(S/2)
fc+(S/2)
Frequency
Amplitude

## Slide 10: Implementation of Binary ASK
An everyday example: IR remote
Digital data are presented as a unipolar NRZ digital signal with a high voltage of 1 V and a low voltage of 0 V
Result: multiply the NRZ digital signal by the carrier signal coming from an oscillator

## Slide 11: Example – ASK Bit Rate
Given bandwidth of 100 kHz, spanning from 200 kHz to 300 kHz
Modulate data using ASK with communication circuitry that requires bandwidth of 2 Hz/baud (d = 1)
What is the carrier frequency and the bit rate?
Solution:

## Slide 12: Full-Duplex ASK
Bandwidth can be divided into two to support full-duplex communication
  Two carrier frequencies are used

## Slide 13: Frequency Shift Keying
frequency of the carrier signal is varied to represent data
  The frequency of the modulated signal is constant for the
duration of one signal element
  but changes for the next signal element if the data element
changes
Both peak amplitude and phase remain constant for all signal elements
Binary FSK (or BFSK)
  consider two carrier frequencies f1 and f2
Multilevel FSK (MFSK)
  more than two frequencies

## Slide 14: Binary Frequency Shift Keying
Consider two carrier frequencies f1 and f2
  first carrier frequency for the data element 0
  Second carrier frequency for the data element 1
  carrier frequencies are very high and the difference between them is very small
Both f1 and f2 are Δf apart from the midpoint between the two bands
The difference between the two frequencies is 2Δf

## Slide 15: Bandwidth for BFSK
carrier signal is only one simple sine wave -> has a continuous set of frequencies
modulation produces a nonperiodic composite signal
Consider FSK is two ASK signals, each with its own carrier frequency (
f1 or f2)
difference between the two frequencies is 2Δf
  minimum value of 2Δf should be at least S for the proper
operation of modulation and demodulation.
B = (1 + d) x S + frequency shift = (1 + d) x S + 2Δf
  S is the signal rate
  B is the bandwidth
  d depends on the modulation and filtering process
  The value of d is between 0 and 1

## Slide 16: BFSK Example
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What should be the carrier frequency and the bit rate if we modulated our data by using FSK with d = 1?
Solution
Same FSK Problem, but we are modulating by using FSK. The midpoint of the band is at 250 kHz. We choose 2Δf to be 50 kHz
bit rate for ASK is 50 kbps while the bit rate for FSK is 25 kbps

## Slide 17: Multilevel FSK
Use one frequency to send more than one bit at a time
E.g., the whole bandwidth divided into 8 frequency ranges- each 2Δf apart.
B = (1 + d) x S + (L - 1) 2Δf → B = L x S
minimum value of 2Δf needs to be S hence d=0
MFSK uses more bandwidth than the other techniques
it should be used when noise is a serious issue

## Slide 18: Multilevel FSK example
We need to send data 3 bits at a time at a bit rate of 3 Mbps. The carrier frequency is 10 MHz. Calculate the number of levels (different frequencies), the baud rate, and the bandwidth.
Solution
We can have L = 23 = 8
The baud rate is S = 3 MHz/3 = 1 Mbaud
This means that the carrier frequencies must be 1 MHz apart (2Δf = 1 MHz)
The bandwidth is B = 8 × 1 = 8 MHz

## Slide 19: Phase Shift Keying
Phase of the carrier is varied to represent two or more different signal elements
Both peak amplitude and frequency remain constant as the phase changes
Today, PSK is more common than ASK or FSK
Binary Phase Shift Keying
  only two signal elements
Quadrature PSK (QPSK)
  uses two separate BPSK modulations

## Slide 20: Binary Phase Shift Keying
Or Binary PSK
only two signal elements
  one with a phase of 0°
  other with a phase of 180°

## Slide 21: Binary PSK
The bandwidth is the same as that for binary ASK, but less than that for BFSK
No bandwidth is wasted for separating two carrier signals
PSK | ASK
PSK is less susceptible to noise than ASK as noise can change the amplitude easier than it can change the phase | ASK is more susceptible to noise than PSK
the criterion for bit detection is the phase of the signal | the criterion for bit detection is the amplitude of the signal
superior to FSK because we do not need two carrier signals | need two carrier signals
needs more sophisticated hardware to be able to distinguish between phases | No sophisticated hardware

## Slide 22: Comparison ASK, FSK, PSK
22
46
Parameters | ASK | FSK | PSK
Variable characteristics | Amplitude | Frequency | Phase
Bandwidth | B =(1+d)S d is due to modulation & filtering ,lies between 0 & 1. | B=(1+d)×S+2Δf | B=(1+d)×S
Noise immunity | low | High | High
Complexity | Simple | Moderately complex | Very complex
Error probability | High | Low | Low
Performance in presence of noise | Poor | Better than ASK | Better than FSK
Bit rate | Suitable upto 100 bits/sec | Suitable upto about 1200 bits/sec | Suitable for high bit rates

## Slide 23: Comparison ASK, FSK, PSK
BASK BFSK
BPSK
QPSK
23
46

## Slide 24: Analog-to-Analog Conversion
Process of transmitting analog information by an analog signal
Although the signal is already analog, modulation is needed if a band-pass channel is available to us eg. Radio
  The government assigns a narrow bandwidth to each radio station
  each radio station – produces low-pass signal
    all stations low analog pass signal in the same range
  Listening to different stations, the low-pass signals need to be shifted, each to a different range  bans pass signal

## Slide 25: Amplitude Modulation (AM)
Amplitude of the carrier signal is modulated to follow the changing
amplitudes of the modulating signal
  Only the amplitude changes to follow variations in the information
  The frequency and phase of the carrier remain the same
The modulating signal is the envelope of the carrier
The amplitude of the carrier signal changed according to the amplitude of the modulating signal using a simple multiplier

## Slide 26: AM Bandwidth
The modulation creates a bandwidth that is twice the bandwidth of the modulating signal and covers a range centered on the carrier frequency
  BAM=2B
As the signal components above and below the carrier frequency carry exactly the same information, some implementations discard one-half of the signals and cut the bandwidth in half.

## Slide 27: Standard Bandwidth Allocation for AM Radio
Bandwidth of an audio signal (speech and music) = usually 5 kHz
AM radio station needs a bandwidth of 10 kHz
  Federal Communications Commission (FCC) allows 10 kHz for each AM station
AM stations are allowed carrier frequencies anywhere between 530 and
1700 kHz (1.7 MHz)
Each station’s carrier frequency must be separated from those on either
side of it by at least 10 kHz (one AM bandwidth) to avoid interference
If one station uses a carrier frequency of 1100 kHz, the next station’s
carrier frequency cannot be lower than 1110 kHz

## Slide 28: Frequency Modulation (FM)
Frequency of the carrier signal is modulated to follow the changing
voltage level (amplitude) of the modulating signal
  Peak amplitude and phase of the carrier signal remain constant,
  As the amplitude of the information signal changes, the frequency of the carrier changes correspondingly
Implemented by using a voltage-controlled oscillator as with FSK
  The frequency of the oscillator changes according to the input voltage which is
the amplitude of the modulating signal

## Slide 29: FM Bandwidth
The actual bandwidth is difficult to determine exactly
Can be shown empirically that it is
  several times that of the analog signal or
  2(1 + β)B where β is a factor that depends on modulation
technique with a common value of 4.

## Slide 30: Standard Bandwidth Allocation for FM Radio
The bandwidth of an audio signal (speech and music) broadcast in stereo is almost 15 kHz
FCC allows 200 kHz (0.2 MHz) for each station
  β = 4 with some extra guard band
FM stations are allowed carrier frequencies anywhere between 88 and 108 MHz
Stations must be separated by at least 200 kHz to keep their bandwidths from overlapping
To create even more privacy, the FCC requires that in a given area, only alternate bandwidth allocations may be used
The others remain unused to prevent any possibility of two stations interfering with each other.
Given 88 to 108 MHz as a range, there are 100 potential FM bandwidths in an area, of
which 50 can operate at any one time

## Slide 31: Phase Modulation (PM)
phase of the carrier signal is modulated to follow the changing voltage level (amplitude) of the modulating signal
  peak amplitude and frequency of the carrier signal remain constant
  As the amplitude of the information signal changes, the phase of the
carrier changes correspondingly
It can be proved mathematically that PM is the same as FM with one difference
  FM: the instantaneous change in the carrier frequency is proportional to
the amplitude of the modulating signal
  PM: the instantaneous change in the carrier frequency is proportional to
the derivative of the amplitude of the modulating signal

## Slide 32: Phase Modulation (PM)
PM is normally implemented by using a voltage-controlled oscillator along with a derivative
Frequency of the oscillator changes according to the derivative of the input voltage, which is the amplitude of the modulating signal.

## Slide 33: PM Bandwidth
The actual bandwidth is difficult to determine exactly, but it can be shown empirically that it is several times that of the analog signal
BPM = 2(1 + β)B
Although the formula shows the same bandwidth for FM and PM, the value of β is lower in the case of PM (around 1 for narrowband and 3 for wideband)

## Slide 34: Summary
Digital-to-analog conversion is the process of changing one of the characteristics of
an analog signal based on the information in the digital data
Digital-to-analog conversion can be accomplished in several ways: amplitude shift keying (ASK), frequency shift keying (FSK), and phase shift keying (PSK)
Quadrature amplitude modulation (QAM) combines ASK and PSK
A constellation diagram shows us the amplitude and phase of a signal element,
particularly when we are using two carriers (one in-phase and one quadrature)
Analog-to-analog conversion is the representation of analog information by an
analog signal
Conversion is needed if the medium is bandpass in nature or if only a bandpass
bandwidth is available to us
Analog-to-analog conversion can be accomplished in three ways: amplitude
modulation (AM), frequency modulation (FM), and phase modulation (PM).

## Slide 35: Homework
Problem from textbook chapter 5 P5.1 to P5.12

## Slide 36: Multiplexing
CS44 Data Communications

## Slide 37: Outline
Multiplexing
  Frequency-Division Multiplexing
  Wavelength-Division Multiplexing
  Time-Division Multiplexing
Spread Spectrum
  Frequency Hopping Spread Spectrum
  Direct Sequence Spread Spectrum

## Slide 38: Multiplexing
Process of combining multiple signals (analog or digital), commonly from slow devices, onto one very fast communications link
  achieved by a device called a Multiplexer (MUX) and Demultiplexer (DEMUX)
    MUX: combines the lines at sender on the left to direct their transmission streams into a single stream (many-to-one)
    DEMUX: separates the stream at receiver back into its component transmissions (one-to-
many) and directs them to their corresponding lines
allow the simultaneous transmission of multiple signals across a single data link
  Link  physical path
  Channel portion of a link that carries a transmission between a given pair of lines
    One link can have many (n) channels

## Slide 39: Multiplexing …
Carrier division multiple access (CDMA) is considered as a fourth multiplexing category
Analog Multiplexing technique to combine analog signals
Analog Multiplexing technique to combine optical signals
Digital multiplexing technique to combine
several low rate channels into high rate one
synchronous
Asynchronous/
statistical

## Slide 40: Frequency Division Multiplexing (FDM)
Can be applied when the bandwidth of a link in (hertz) is greater than the combined bandwidths of the signal to be transmitted
  Medium BW > Channel BW
Transmitting all of the signals along the same high speed link simultaneously

## Slide 41: FDM …
Each signal is modulated to a different carrier frequency
  Carrier frequencies are separated by sufficient bandwidth to
accommodate the modulated signal
    These bandwidth ranges are the channels through which the various signals travel
      Channels can be separated by strips of unused bandwidth -guard bands -to prevent signals from overlapping
    In addition, carrier frequencies must not interfere with the original data frequencies
These modulated signals are then combined into a single composite signal that can be transported by the link
E.g., broadcast radio
Channel allocated even if no data

## Slide 42: Conceptual View of FDM
Channel 3
Channel 2
Channel 1
f1
f2
f3

## Slide 43: FDM for digital signal
Even though FDM is analog multiplexing technique; it can be used to combine sources sending digital signals
A digital signal can be converted to an analog signal before FDM is used to multiplex them

## Slide 44: FDM: Multiplexing Process
Each source generates
a signal of a similar
frequency range
similar signals modulate different carrier frequencies ( f1, f2, and f3)
combined  a single composite signal that is sent out over a media link that
has enough bandwidth to accommodate it.

## Slide 45: FDM: Demultiplexing Process
series of filters to decompose the multiplexed signal into its constituent component signals
separates the signals from their carriers and passes them to the output lines

## Slide 46
Strips of unused bandwidth to prevent signals from overlapping
FDM
3 kHz
f
f
3 kHz
3 kHz
3 kHz
FDM
(no guard band)
FDM
(with guard band)
f
3 kHz
3 kHz
3 kHz
f
3 kHz
f
3 kHz
3 kHz
3 kHz

## Slide 47
Assume that a voice channel occupies a bandwidth of 4 kHz. We need to combine three voice channels into a link with a bandwidth of 12 kHz, from 20 to 32 kHz. Show the configuration, using the frequency domain. Assume there are no guard bands.
Solution
We shift (modulate) each of the three voice channels to a different bandwidth
  20- to 24-kHz bandwidth for the first channel
  24- to 28-kHz bandwidth for the second channel
  28- to 32-kHz bandwidth for the third one

## Slide 49
Five voice channels, each with 3-kHz bandwidth, are to be multiplexed together.
If there is a need for a guard band of 1.5 kHz, what is the minimum bandwidth of the link?
f
3 kHz
3 kHz
3 kHz
3 kHz
3 kHz
1.5 kHz
1.5 kHz
1.5 kHz
1.5 kHz
21 kHz

## Slide 50
Four digital-data channels, 1 Mbps each, use a satellite channel of 1 MHz. Design an appropriate configuration using FDM. (assume 1 Hz/baud)
The satellite channel is analog
Divide it into four channels, each channel having a 250-kHz bandwidth
Each digital channel of 1 Mbps is modulated so that each 4 bits is modulated to 1 Hz. One solution is 16-QAM modulation

## Slide 51
Traditionally multiplexed signals from lower-bandwidth lines onto higher-bandwidth lines to maximize the efficiency
  Many switched or leased lines can be combined into fewer but bigger channels
    For analog lines, FDM is used
Example of hierarchical systems (analog hierarchy) used by telephone companies
  made up of groups, supergroups, master groups, and jumbo groups

## Slide 52
F D M
F D M
F D M
F D M
5 groups
…
10 supergropus
6 master groups
group
supergroup
master group
Jumbo group
4 kHz
4 kHz
4 kHz
…
12 voice channels
Used by AT&T (from 1910s to early 1980s)
48 kHz
12 voice channels
240 kHz
60 voice channels
2.52 MHz
600 voice channels
16.984 MHz
3600 voice channels

## Slide 53
First level:
  12 voice channels are multiplexed onto a higher-bandwidth line to
create a group
  A group has 48 kHz of bandwidth and supports 12 voice channels
Group level:
  Up to five groups can be multiplexed to create a composite signal called a supergroup
  A supergroup has a bandwidth of 240 kHz and supports up to 60 voice channels
  Supergroups can be made up of either five groups or 60
independent voice channels

## Slide 54
Supergroups level
  10 supergroups are multiplexed to create a master group
  A master group must have 2.40 MHz of bandwidth, but the need for guard bands between the supergroups increases the necessary bandwidth to 2.52 MHz
  Master groups support up to 600 voice channels.
Jumbo group Level
  six master groups can be combined into a jumbo group
  A jumbo group must have 15.12 MHz (6 × 2.52 MHz) but is augmented to 16.984 MHz to allow for guard bands between the master groups

## Slide 55
Common application of FDM is AM and FM radio broadcasting
Radio uses the air as the transmission medium
  AM uses special band from 530 to 1700 kHz
    All radio stations need to share this band
    each AM station needs 10kHz of bandwidth
    Each station uses a different carrier frequency which means it is shifting its signal and multiplexing
  FM has a wider band of 88 to 108 MHz - each station needs a bandwidth of 200 kHz
television broadcasting- Each TV channel has its own bandwidth of 6 MHz

## Slide 56
The first generation of cellular telephones also uses FDM
  Each user is assigned two 30-kHz channels, one for sending voice
and the other for receiving
    The voice signal, which has a bandwidth of 3 kHz (from 300 to 3300 Hz), is modulated by using FM
    An FM signal has a bandwidth 10 times that of the modulating signal.
      each channel has 30 kHz (10 × 3) of bandwidth
      each user is given, by the base station, a 60-kHz bandwidth in a range available at the time of the call

## Slide 57
The Advanced Mobile Phone System (AMPS) uses two bands
  The first band of 824 to 849 MHz is used for sending,
  869 to 894 MHz is used for receiving (Each band is 25 MHz)
  Each user has a bandwidth of 30 kHz in each direction
  If we divide 25 MHz by 30 kHz, we get 833.33
    In reality, the band is divided into 832 channels
    Of these, 42 channels are used for control, which means only 790 channels are available for cellular phone users.

## Slide 58
In radio and television broadcasting, there is no physical multiplexer or demultiplexer
  the stations agree to send their broadcasts to the air using different carrier frequencies
In cellular telephone system, a base station needs to assign a carrier frequency to the telephone user
  When a user hangs up, her or his bandwidth is assigned to another caller

## Slide 59
digital process that allows several connections to share the high bandwidth of a link
Time is shared
  Each connection occupies a portion of time in the link
  Same link of FDM is shown sectioned by time rather than by
frequency
Digital data from different sources are combined into one timeshared link
Analog data can be sampled, changed to digital data, and then multiplexed by using TDM

## Slide 60
33
33
Channel 1
Channel 2
Channel 3
Channel 1
Channel 2
Channel 3
Channel 1
Channel 2
Channel 3
M U X
2
3
3 | 2 | 1 | 3 | 2 | 1 | 3 | 2 | 1
1 1
2
3
D E M U X
Data flow
Portions of signals 1, 2, and 3
occupy the link sequentially
Data in a message from source 1 always go to one specific destination 1, 2, 3, or 4
The delivery is fixed and unvarying, unlike switching

## Slide 61
Synchronous TDM: each input connection has an allotment in the output even if it is not sending data
  Time Slots and Frames
  Interleaving
  Empty Slots
  Data Rate Management
  Frame Synchronizing
  Applications
    Digital Signal Service
    T Lines
    T Lines for Analog Transmission
    E Lines
    More Synchronous TDM Applications
Statistical TDM : slots are dynamically allocated to improve bandwidth efficiency
  Addressing
  Slot Size
  No Synchronization Bit
  Bandwidth

## Slide 62
Medium Data Rate > Signal Data Rate
Multiple digital signals interleaved in time
Time slots
are preassigned to sources and fixed
are allocated even if no data
do not have to be evenly distributed among sources
Time slots are grouped into frames
  A frame consists of one complete cycle of time slots, with one slot dedicated to each sending device
T D M
A
B
C
C | B | A | C | B | A | C | B | A
Frame
Time slot
one unit

## Slide 63
each input connection is divided into units
Each input unit becomes one output unit
Duration of an output time slot is n times shorter than the duration of an input time slot
  If an input time slot is T s, the output time slot is T/n s, where n is the number of connections
    a unit in the output connection has a shorter duration; it travels faster

## Slide 64
In Figure, the data rate for each input connection is 1 kbps. If 1 bit at a time is
multiplexed (a unit is 1 bit), what is the duration of (1) each input slot, (2) each
output slot, and (3) each frame?
Solution : The data rate of each input connection is 1 kbps.
Bit duration is 1/1000 s or 1 ms. The duration of the input time slot is 1 ms (same as bit duration).
The duration of each output time slot is one-third of the input time slot. This
means that the duration of the output time slot is 1/3 ms.
3. Each frame carries three output time slots. So the duration of a frame is 3 × 1/3 ms, or 1 ms. The duration of a frame is the same as the duration of an input unit.

## Slide 65
Figure shows synchronous TDM with a data stream for each input and one data stream for the output. The unit of data is 1 bit. Find
•
the input bit duration: 1/1 Mbps = 1 μs
the output bit duration: 1/4 μs
the output bit rate: 4 Mbps
the output frame rate: 1,000,000 frames per second

## Slide 66
Four 1-kbps connections are multiplexed together. A unit is 1 bit. Find
the duration of 1 bit before multiplexing: 1/1 kbps, or
0.001 s (1 ms).
the transmission rate of the link: is 4 times the rate of a connection, or 4 kbps
the duration of a time slot: 1/4 ms or 250 μs
the duration of a frame: 1 ms

## Slide 67
TDM can be visualized as two fast-rotating switches
  one on the multiplexing side
    interleaving : the switch opens in front of a connection, that connection has the opportunity to send a unit onto the path
  other on the demultiplexing side
    opens in front of a connection, that connection has the opportunity to receive a unit from the path
switches  synchronized and rotate at the same speed, but in opposite directions
Connection
Interleaving Process

## Slide 68
Four channels are multiplexed using TDM. If each channel
sends 100 bytes/s and we multiplex 1 byte per channel. Show the
frame traveling on the link: 1 byte from each channel
size of the frame; 4 bytes, or 32 bits
duration of a frame: 1/100 s
frame rate: 100 frames per second
bit rate for the link: 100 × 32, or 3200 bps
  .

## Slide 69
A multiplexer combines four 100-kbps channels using a time slot of 2 bits. Show the output with four arbitrary inputs.
What is the frame rate? - 50,000 frames per second
What is the frame duration? - 1/50,000 s or 20 μs
What is the bit rate? – frame rate x bits per frame
= 50,000 × 8 = 400,000 bits/400 kbps
What is the bit duration? - 1/400,000 s, or 2.5 μs

## Slide 70
Synchronous TDM  not efficient
  If a source does not have data to send, the corresponding slot in
the output frame is empty
No frame is full
statistical TDM can improve the efficiency by removing the empty slots from the frame

## Slide 72
how to handle a disparity in the input data rates?
  Data rates of all input lines are same?
  If data rates are not the same, use one or combination of three strategies
    multilevel multiplexing
    multiple-slot allocation
    pulse stuffing

## Slide 73
used when the data rate of an input line is a multiple of others
For example, we have two inputs of 20 kbps and three inputs of 40 kbps
  The first two input lines can be multiplexed together to provide a data rate equal to the last three
  A second level of multiplexing can create an output of 160 kbps

## Slide 74
More efficient to allot more than one slot in a frame to a single input line
For example, we might have an input line that has a data rate that is a multiple of another input
Input line with a 50-kbps data rate can be given two slots in the output. We insert a demultiplexer in the line to make two inputs out of one.

## Slide 75
Sometimes the bit rates of sources are not multiple integers of each other
make the highest input data rate the dominant data rate and then add dummy bits to the input lines with lower rates  increase their rates
called pulse stuffing, bit padding, or bit stuffing
The input with a data rate of 46 is pulse-stuffed to increase the rate to 50 kbps. Now multiplexing can take place.

## Slide 76
Multiplexer and demultiplexer must be synchronized
  If not synchronized, a bit belonging to one channel may be
received by the wrong channel
Framing bits added at beginning of each frame are used to provide synchronization
  follow a pattern from frame to frame

## Slide 77
Synchronization pattern: allows the demultiplexer to synchronize with the incoming stream so that it can separate the time slots accurately
Synchronization pattern
C | B | A | 1
… 1 0 1 0 …
framing bit
C | B | A | 0
C | B | A | 1
C | B | A | 0

## Slide 78
Four sources, each creating 250 characters per second. If the interleaved unit is a character and 1 synchronizing bit is added to each frame, find
the data rate of each source : 250 × 8 = 2000 bps = 2 kbps
duration of each character in each source : 1/250 s, or 4 ms
frame rate: 250 frames per second
duration of each frame: 1/250 s, or 4 ms
number of bits in each frame : 4 × 8 + 1 = 33 bits
data rate of the link : 250 × 33, or 8250 bps
Bit rates of four channels =8000 bps. Because 250 frames are traveling per second and each contains 1 extra bit for synchronizing, extra 250 bit for data rate of the link

## Slide 79
Two channels, one with a bit rate of 100 kbps and another with a bit rate of 200 kbps, are to be multiplexed
How this can be achieved?
  Allocate one slot to the first channel and two slots to the second channel. Each frame carries 3 bits.
What is the frame rate?
100,000 frames per second because it carries 1 bit from the first channel
What is the frame duration?
  1/100,000 s, or 10 ms
What is the bit rate of the link?
  The bit rate is 100,000 frames/s × 3 bits per frame, or 300 kbps
Note that because each frame carries 1 bit from the first channel,
the bit rate for the first channel is preserved. The bit rate for the
second channel is also preserved because each frame carries 2 bits from the second channel.

## Slide 80
Some second-generation cellular telephone companies use synchronous TDM
  digital version of cellular telephony
    divides the available bandwidth into 30-kHz bands
      For each band, TDM is applied so that six users can share the band
        each 30-kHz band is now made of six time slots, and the digitized voice signals of the users are inserted in the slots
        the number of telephone users in each area is now 6 times greater

## Slide 81
synchronous TDM - each input has a reserved slot in the output frame
  inefficient if some input lines have no data to send
    Solution : dynamically allocate slots to improve bandwidth efficiency
      statistical time-division multiplexing : Only when an input line has a slot’s worth of data to send is it given a slot in the output frame
        the number of slots in each frame is less than the number of input lines
        The multiplexer checks each input line in round robin fashion; it allocates a slot for an input line if the line has data to send; otherwise, it skips the line and checks the next line

## Slide 83
PArameter | Synchronous-TDM | Statistical-TDM
Output slot | totally occupied by data | needs to carry data as well as the address of the destination
Addressing | No need | Required - simplest form can be n bits to define N different output lines with n = log2 N
Relationship b/w the i/p and o/p | synchronization and this preassigned relationships serve as an address | Not preassigned
Slot Size | the data size | the ratio of the data size to address size must be reasonable to make transmission efficient Eg. inefficient to send 1 bit per slot as data when the address is 3 bits
Frame synchronization | Need to synchronize – require synchronization bits | need not be synchronized – no synchronization bit
Capacity of the link (Bandwidth) | Greater than or equal to sum of the capacities of each channel | Less than the sum of the capacities of each channel. During peak times, some slots need to wait

## Slide 84
Multiplexing and spread spectrum  combines signals from several sources to fit into a larger bandwidth
Multiplexing goal - to achieve bandwidth efficiency
Spread spectrum goal
  designed to be used in wireless applications (LANs and WANs)
    wireless applications all stations use air (or a vacuum) as the medium for communication
    Air/vacuum is shared medium with challenge
      Stations must be able to share this medium without interception by an eavesdropper and without being subject to jamming from a malicious intruder
How to achieve this goal?
  Use spread spectrum techniques that add redundancy

## Slide 85
If the required bandwidth for each station is B, spread spectrum expands it to Bss, such that Bss >> B
  The expanded bandwidth allows the source to wrap its message in a protective envelope for a more secure transmission
Eg. An analogy is the sending of a delicate, expensive gift
We can insert the gift in a special box to prevent it from being damaged during transportation, and we can use a superior delivery service to guarantee the safety of the package

## Slide 86
Used to achieves its goals:
  The bandwidth allocated to each station needs to be larger than
what is needed -- allows redundancy
  Spreading process/code expands the original bandwidth B to the bandwidth Bss -- occurs independently after the original signal is created by the source
    The spreading code is a series of numbers that look random, but are actually a pattern
There are two techniques to spread the bandwidth:
  Frequency Hopping Spread Spectrum (FHSS)
  Direct Sequence Spread Spectrum (DSSS)

## Slide 87
Uses M different carrier frequencies that are modulated by the source signal done using one carrier frequency at a time
  At one moment, the signal modulates one carrier frequency; at the next moment, the signal modulates another carrier frequency
  bandwidth occupied by a source after spreading is BFHSS >> B.
Creates a k-bit pattern for every hopping period Th
Creates a carrier signal of the chosen frequency
Find the frequency using k- bit pattern to be used for this hopping period

## Slide 88
Consider eight hopping frequencies - extremely low for real applications and is just for illustration
  M is 8 and k is 3
Pseudorandom code generator will create eight different 3- bit patterns - repeated after eight hoppings
  mapped to eight different frequencies in the frequency table
  Assume the required bandwidth of the original signal is 100 kHz

## Slide 89
required bandwidth of the original signal is 100 kHz
Repeat | at hopping period (At start t=1) | k-bit pattern | frequency selected- source signal modulates this carrier frequency
 | t*1 | 101 | 700 kHz
 | t*2 | 111 | 900-kHz
 | t*3 | 001 | 300-kHz
t=t+1 | t*4 | 000 | 200-kHz
 | t*5 | 010 | 400-kHz
 | t*6 | 110 | 800-kHz
 | t*7 | 011 | 500-kHz
 | t*8 | 100 | 600-kHz

## Slide 90
Privacy effect - If an intruder tries to intercept the transmitted signal, she can only access a small piece of data because she does not know the spreading sequence to quickly adapt herself to the next hop
Antijamming effect- A malicious sender may be able to send noise to jam the signal for one hopping period (randomly), but not for the whole period

## Slide 91
M =number of hopping frequencies
  can multiplex M channels into one by using the same Bss bandwidth
as a station uses just one frequency in each hopping period
M=4
  FDM – each station uses 1/M of the bandwidth (allocation is fixed)
  FHSS - each station uses 1/M of the bandwidth (allocation changes hop to hop)  multiple FSK (MFSK)

## Slide 92
Expands the bandwidth of the original signal by replacing each data bit with n bits using a spreading code
  Each bit is assigned a code of n bits, called chips
    Chip-rate = n * data-bit

## Slide 93
Consider the sequence used in a wireless LAN is the famous Barker sequence, where n is 11
Assume that the original signal and the chips in the chip generator use polar NRZ encoding
rate is N
11 chips rate is 11N

## Slide 94
Privacy goal - if the intruder does not know the code
Immunity against interference if each station uses a different code

## Slide 95
If a spreading code that spreads signals (from different stations) cannot be combined and separated, bandwidth cannot be shared
  Eg. some wireless LANs
If a special type of sequence code that allows the combining and separating of spread signals, bandwidth can be shared
  Eg. cellular telephony

## Slide 96
FHSS | DSSS
Multiple frequencies are used | Single frequency is used
Hard to find the user’s frequency at any instant of time | User frequency, once allotted is always the same
Frequency reuse is allowed | Frequency reuse is not allowed
Sender need not wait | Sender has to wait if the spectrum is busy
Power strength of the signal is high | Power strength of the signal is low
Stronger and penetrates through the obstacles | It is weaker compared to FHSS
It is never affected by interference | It can be affected by interference
It is cheaper | It is expensive
This is the commonly used technique | This technique is not frequently used

## Slide 97
Multiplexing is a method of combining multiple narrow- band signals into a wider-band signal
FDM multiplexes signals into different frequencies
TDM multiplexes signals into different time slots
FHSS - At one moment, the signal modulates one carrier frequency; at the next moment, the signal modulates another carrier frequency
DSSS - replace each data bit with n bits using a spreading code

## Slide 98
Problem form chapter 6: P6.1 to P6.18

## Slide 99
CS44 Data Communications

## Slide 100
100
Circuit-switched Networks
  Three Phases
  Efficiency
  Delay
Packet Switching
  Datagram Networks
  Virtual-Circuit Networks

## Slide 101
101
Network - Connect multiple devices
How to connect them to make one-to-one communication possible?
  a point to point connection in between pair of devices (mesh topology) - increases the number of connection
  Use network topology - wasteful and impractical for very large
network
  a better solution for this situation is Switching
    can be discussed at the physical layer, data-link layer, network layer, and application layer
      circuit-switching - occurs at the physical layer
      packet-switching - occurs at the data-link and network layers
      message switching – occurs logically at the application layer

## Slide 102
A switched network is made up of a series of interconnected nodes called switches
Switches are devices capable of creating temporary connections between
two or more devices linked to the switch
The end systems (communicating devices) - labeled A, B, C, D, and so on
Switches -labeled I, II, III, IV, and V
Each switch is connected to multiple links.
102

## Slide 103
Switching is a process moving data from one interface and delivering it through another interface, selecting the best paths between machines that stores messages
Types of switching methods
  Circuit Switching
  Packet Switching - further be divided into virtual circuit approach and datagram approach
  Message Switching
103

## Slide 104
104
Physical Layer - only circuit switching
  no packets exchanged at the physical layer
  switches at the physical layer allow signals to travel in one path or another
Data-Link Layer - packet switching
  packet in this case means frames or cells
  done using a virtual-circuit approach
Network Layer - packet switching
  either a virtual-circuit approach or a datagram approach can be used
Application Layer - only message switching
  message-switched communication - exchange messages

## Slide 105: Circuit-switched network
105
Consists of a set of switches connected by physical links
A connection between two stations is a dedicated path made of one or more links
  Each connection uses only one dedicated channel on each link
  Each link is normally divided into n channels by using FDM or TDM

## Slide 106
multiplexing can be implicitly included in the switch fabric
Circuit-switched network with four switches and four links
  Each link is divided into n (n =3) channels by using FDM or TDM
End systems - computers or telephones- directly connected to a switch
106

## Slide 107
10
End system A needs to communicate with end system M
  System A needs to request a connection to M that must be accepted by
all switches as well as by M itself - called the setup phase
    Circuit switching takes place at the physical layer
  Stations reserves the resources (such as channels (bandwidth in FDM and time slots in TDM) on each link, switch buffers, switch processing time, and switch input/output ports) to be used during the communication for the entire duration of data transfer until the teardown phase
    Combination of circuits or channels defines the dedicated path which is established for data- transfer phase
    Data transferred between the two stations are not packetized (physical layer transfer of the signal)
    no addressing involved during data transfer - switches route the data based on their occupied band (FDM) or time slot (TDM)
  After all data have been transferred, the circuits are torn down
    When one of the parties needs to disconnect, a signal is sent to each switch to release the resources.
Requires three phases: connection setup, data transfer, and connection teardown

## Slide 108
Before the two parties (or multiple parties in a conference call) can communicate, a dedicated circuit (combination of channels in links) needs to be established
The end systems are normally connected through dedicated lines to the switches, so connection setup means creating dedicated channels between the switches
  when system A needs to connect to system M,
    it sends a setup request that includes the address of system M, to switch I
      end-to-end addressing is required for creating a connection between the two end systems
        Example, the addresses of the computers assigned by the administrator in a TDM network, or telephone numbers in an FDM network
    Switch I finds a channel between itself and switch IV that can be dedicated for this purpose
    Switch I then sends the request to switch IV, which finds a dedicated channel between itself and switch III
    Switch III informs system M of system A’s intention at this time
an acknowledgment from system M needs to be sent in the opposite direction to system A
  Only after system A receives this acknowledgment is the connection established.

## Slide 109: Circuit-switched network Example 1
Connect eight telephones in a small area. The switch controls the connections
  Communication is through 4-kHz voice channels
  Assume that each link uses FDM to connect a maximum of two voice channels
    The bandwidth of each link is then 8 kHz
Telephone 1 is connected to telephone 7; 2 to
5; 3 to 8; and 4 to
6.

## Slide 110: Circuit-switched network Example 2
A circuit-switched network that connects computers in two remote offices of a private company
  The offices are connected using a T-1 line leased from a communication service provider
There are two 4 × 8 (4 inputs and 8 outputs) switches in this network
  For each switch, four output ports are folded into the input ports to allow communication between computers in the same office
  Four other output ports allow communication between the two offices

## Slide 111
not as efficient because resources are allocated during the entire duration of the connection
  These resources are unavailable to other connections
In a telephone network, people normally terminate the communication when they have finished their conversation but, in computer networks, a computer can be connected to another computer even if there is no activity for a long time
  In this case, allowing resources to be dedicated means that other connections are deprived.

## Slide 112
Minimal delay
During data transfer, the data are not delayed at each switch; the resources are allocated for the duration of the connection
Delay in a circuit-switched network when only two switches are involved

## Slide 113
No waiting time at each switch
The total delay is due to the time needed to
  create the connection: sum of four parts:
    the propagation time of the source computer request , the request signal transfer time, the propagation time of the acknowledgment from the destination computer, and the signal transfer time of the acknowledgment
  transfer data can be very long: sum of two parts: the propagation time and data transfer time
  disconnect the circuit

## Slide 114: Packet-switched network
divides the data into packets of fixed or variable size.
  The size of the packet is determined by the network and the governing protocol.
no resource reservation - resources are allocated on demand
– first-come, first-served basis
lack of reservation may create delay
classified as
  Datagram Networks
  Virtual circuit Networks

## Slide 115: Datagram Networks
Operates at the Network layer
Each packet is treated independently of all others
  Even if a packet is part of a multipacket transmission, the network treats packets as though they existed alone
  Each packet of one message can travel a different route towards their final destination
Packets are referred to as datagrams
Datagram approach - to deliver four packets from station A to station X
4
3
2
1
4
3 1
2
1
1
2
3
4
4
3
2
1
Here, switches – referred
as routers
Different symbol used for the switches

## Slide 116: Datagram Networks …
All four packets (or datagrams) belong to the same message, but may travel different paths to reach their destination
  links may be involved in carrying packets from other sources and do not have the necessary bandwidth available to carry all the packets from A to X
Destination may receive datagrams out of order with different delays between the packets
Packets may also be lost or dropped because of a lack of resources
  Upper-layer protocol reorder the datagrams or ask for lost datagrams before passing them on to the application

## Slide 117: Datagram Networks …
The datagram networks connectionless networks
  Switch (packet switch) does not keep information about the
connection state
  no setup or teardown phase
    how are the packets routed to their destinations in a datagram network?
      Through routing table of a switch

## Slide 118: Datagram Networks- Routing Table
Each switch (or packet switch) has a routing table
  based on the destination address
  dynamic and are updated periodically
The destination addresses and the corresponding forwarding output ports are recorded in the tables
This is different from the table of a circuit-switched network in which each entry is created
when the setup phase is completed and deleted when the teardown phase is over

## Slide 119: Datagram Networks- Routing Table
The destination address in the header of a packet in a datagram network remains the same during the entire journey of the packet.
When the switch receives the packet, this destination address is examined; the routing table is consulted to find the corresponding port through which the packet should be forwarded
The packet header contains a sequence number in the header so it can be ordered at the destination.
A circuit switched network does not require a header or destination address for the data transfer stage, the link is dedicated!

## Slide 120: Datagram Networks- Efficiency
better than that of a circuit-switched network
resources are allocated only when there are packets to be transferred
If a source sends a packet and there is a delay of a few minutes before another packet can be sent, the resources can be reallocated during these minutes for other packets from other sources.

## Slide 121: Datagram Networks- Delay
There may be greater delay in a datagram network than in a virtual-circuit network
Although there are no setup and teardown phases, each packet may experience a wait at a switch before it is forwarded
In addition, since not all packets in a message necessarily travel through the same switches, the delay is not uniform for the packets of a message.

## Slide 122: Datagram Networks- Delay
The packet travels through two switches
There are three transmission times (3T), three propagation delays (slopes 3τ of the lines), and two waiting times (w1 + w2)
ignore the processing time in each switch
The total delay is 3T + 3τ+ w1 + w2

## Slide 123: Virtual-Circuit Networks
cross between a circuit-switched network and a datagram network
shares characteristics of both
  As in a circuit-switched network, there are setup and teardown phases in addition to the data transfer phase.
  Resources can be allocated during the setup phase, as in a circuit- switched network, or on demand, as in a datagram network.
  As in a datagram network, data are packetized and each packet carries an
address in the header. However, the address in the header has local
jurisdiction (it defines what the next switch should be and the channel on which the packet is being carried), not end-to-end jurisdiction
  As in a circuit-switched network, all packets follow the same path established during the connection.
  A virtual-circuit network is normally implemented in the data-link layer,
while a circuit-switched network is implemented in the physical layer and a datagram network in the network layer

## Slide 124
The network has switches that allow traffic from sources to destinations

## Slide 125
VCN behaves like a circuit switched net because there is a setup phase to establish the VCI entries in the switch table; there is also a data transfer phase and teardown phase.
  Setup: the source and destination use their global addresses to help switches make table entries for the connection
  Data transfer: transfer a frame from a source to its destination
  Teardown: the source and destination inform the switches to delete the corresponding entry

## Slide 126
All switches on the route between current source to its destination need to have a table entry for that virtual circuit
Switch holds four pieces of information for each virtual circuit that is already set up in its a table with 4 columns:
Inputs half
  Input Port Number
  Input VCI
Outputs half
  Output Port Number
  Output VCI

## Slide 127
A frame arriving at port 1 with a VCI of 14. When the frame arrives, the switch looks in its table to find port 1 and a VCI of 14
When it is found, the switch knows to change the VCI to 22 and send out the frame from port 3

## Slide 128
How a frame from source A reaches destination B and how its VCI changes during the trip?
  Each switch changes the VCI and routes the frame
The data-transfer phase is active until the source sends all its frames to the destination.
The procedure at the switch is the same for each frame of a message
The process creates a virtual circuit, not a real circuit, between the source and destination

## Slide 129
A switch creates an entry for a virtual circuit
  Eg., suppose source A needs to create a virtual circuit to B
Two steps are required:
  setup request: sent from the source to the destination
  acknowledgment : sent from the destination to the source

## Slide 130
34
a. Source A sends a
setup frame to switch 1.
b. Switch 1 receives the setup request frame. It knows that a frame going from A to B goes out through port
3. The switch acts as a packet switch; it has a routing table which is different from the switching table. For the moment, assume that it knows the output port. The switch creates an entry in its table for this virtual circuit, but it is only able to fill three of the four columns. The switch assigns the incoming port (1) and chooses an available incoming VCI (14) and the outgoing port (3). It does not yet know the outgoing VCI, which will be found during the acknowledgment step. The switch then forwards the frame through port 3 to
switch 2.
c. Switch 2 receives the setup request frame. The same events happen here as at switch 1; three columns of the table are completed: in this case, incoming port (1), incoming VCI (66), and outgoing port (2).
e. Destination B receives the setup frame, and if it is ready to receive frames from A, it assigns a VCI to the incoming frames that come from A, in this case 77. This VCI lets the destination know that the frames come from A, and not other sources.
d. Switch 3 receives the setup request frame. Again, three columns are completed: incoming port (2), incoming VCI (22), and outgoing port (3).

## Slide 131
completes the entries in the switching tables
a. The destination sends an acknowledgment to switch 3. The acknowledgment carries the global source and destination addresses so the switch knows which entry in the table is to be completed. The frame also carries VCI 77, chosen by the destination as the incoming VCI for frames from A. Switch 3 uses this VCI to complete the outgoing VCI column for this entry.
e. The source uses this as the outgoing VCI for the data frames to be sent to destination B.
d. Finally switch 1 sends an acknowledgment to source A that contains its incoming VCI in the table, chosen in the previous step.
c. Switch 2 sends an acknowledgment to switch 1 that contains its incoming VCI in the table, chosen in the previous step. Switch 1 uses this as the outgoing VCI in the table.
b. Switch 3 sends an acknowledgment to switch 2 that contains its incoming VCI in the table, chosen in the previous step. Switch 2 uses this as the outgoing VCI in the table.

## Slide 132
In this phase, source A, after sending all frames to B, sends a special frame called a teardown request.
Destination B responds with a teardown confirmation frame.
All switches delete the corresponding entry from their tables.

## Slide 133
resource reservation in a virtual-circuit network can be
  made during the setup or
    the delay for each packet is the same
  can be on demand during the data-transfer phase
    each packet may encounter different delays
    The source can check the availability of the resources, without actually reserving it.
Switching at the data-link layer in a switched WAN such as ATM networks is normally implemented by using virtual- circuit techniques.

## Slide 134
If resources are allocated during the setup phase, there is no wait time for individual packets
The packet is traveling through two switches (routers)
There are three transmission times (3T ), three propagation times (3τ), data transfer depicted by the sloping lines, a setup delay (which includes transmission and propagation in two directions), and a teardown delay (which includes transmission and propagation in one direction).
Ignoring the processing time in each switch, the total delay time is
Total delay = 3T + 3τ + setup delay + teardown delay